## Slide 1
Connor W. Coley Assistant Professor MIT Chemical Engineering MIT Electrical Engineering and Computer Science
ML for Therapeutic Design
March 3, 2022
Data-driven chemistry, small molecule synthesis, and design

## Slide 2: What goes into the >$2B cost of each new drug?

## Slide 3: Small molecules are ubiquitous, even beyond pharma

## Slide 4: Hypothesis-driven molecular discovery is used to identify new molecules that meet certain functional specifications
Overarching theme: computation can accelerate discovery
(by making it easier to generate and test hypotheses)
Validation
Belief
Information
Hypothesis
Goal
Discovery
Property profile
QSAR/QSPR
Synthesis & assaying
Viable candidate
design
synthesize
molecules
and

## Slide 5: Machine learning for molecules Property prediction, screening, and generation

## Slide 6: Evaluating candidate molecules with surrogate models that “replace” experiments or simulations
Models that map molecular structures to properties are ubiquitous in drug design and cheminformatics!
To use ML machinery like neural networks, however, we need to decide on a proper representation that is compatible with our model
Learned
MW
CLogP
Num. atoms
etc.
Fixed
Descriptors
Structural fingerprints
{Physical, Chemical, Biological} property
Feature engineering approach

## Slide 7: Molecular “fingerprints” reflect substructural information
“Key” fingerprints
Circular fingerprints
Each index in a vector corresponds to the presence or absence of a specific substructure
1 2 1 0 1 0 0 1 3 0 …

## Slide 8: Evaluating candidate molecules with surrogate models that “replace” experiments or simulations
Models that map molecular structures to properties are ubiquitous in drug design and cheminformatics!
To use ML machinery like neural networks, however, we need to decide on a proper representation that is compatible with our model
Learned
MW
CLogP
Num. atoms
etc.
Learned
Learned
Fixed
Descriptors
Structural fingerprints
or
{Physical, Chemical, Biological} property
{Physical, Chemical, Biological} property
≥2015
Feature engineering approach
Representation learning approach

## Slide 9: Many choices for representations and regression models
Graph-based and 3D geometry-based representations are useful for distinct applications depending on whether we care about propoertiies of a molecule or properties of a single conformer

## Slide 10: Message passing neural networks (MPNNs)
Fingerprint
Exchange neighbor information
Aqueous solubility
Toxicity
Lipophilicity
Melting point
Atom-, bond-level attributes
Sum over atoms
Message passing networks let information flow between atoms/bonds in a molecular graph to learn a vector representation that can be used for property prediction
Also a natural choice for crystals and other periodic materials!
calculate messages based on neighbors
update atom representations
aggregate over all atoms
initialize
loop

## Slide 11: Evaluating candidate molecules with surrogate models that “replace” experiments or simulations
Training on experimental data
ML models fit to experimental data (e.g., bioactivity measurements) map molecular structures to numerical properties and serve as “surrogates” for the experiments
  One goal is to generalize to molecules w/o data (that we can’t simulate)
Training on simulated data
ML models fit to simulated data (e.g., electronic structure calculations, forces from ab initio molecular dynamics simulations) serve the same role as surrogates for simulations
  One goal is to reduce computational cost
OrbNet
ANI
Chemprop

## Slide 12: Accelerating virtual screening with surrogate models
>100 million candidates
>100 million candidates
Exhaustive screening
Selective
screening
Finds ~90% of best 50k with 2.4% of simulations
Model-guided optimization reduces the cost of virtual screening (e.g., structure-based drug design) by identifying unpromising regions of chemical space
This strategy does not improve the accuracy or fidelity of the docking calculation; it merely speeds its use in screening

## Slide 13: Inverse design as a substitute for virtual screening
Surrogate models can be used in virtual screening to identify high-performing molecules
Generative models can in principle search a larger chemical space
  Genetic algorithms have been used for decades
  Modern trend: “deep generative models” using VAEs, GANs, RL, etc.
Searching a larger chemical space doesn’t guarantee that we’ll find “better” molecules; how we explore the space is important

## Slide 14: Example: hit expansion for DDR1 kinase inhibitor
GAN + RL generative method proposed 30,000 structures
Filters, heuristics, clustering, etc. used to narrow down to 40
Manual synthetic accessibility assessment used to narrow down to 6

## Slide 15: The downside of many de novo generation tools
These AI models optimize whatever black box function you tell them to; if that function doesn’t consider stability or synthesizability, then…*
SMILES GA suggestion scoring 0.881/1.000 on a standard benchmark task
Renz et al. 10.26434/chemrxiv.12213542.v1
Zhou et al., Sci. Rep. 2019, 9
Less obviously bad:

## Slide 16: Synthesizability is an unforgiving, nonlinear function
Intuitive and subjective concept
Highly nonlinear with respect to chemical structure
  Sensitive to availability of key building blocks and selectivity of reactions
ribavirin
easily made from ribose
not ribavirin
much harder to make

## Slide 17: Predictive chemistry Facilitating the synthesis of new molecules

## Slide 18: Assessing synthesizability by planning synthetic routes
Reactants
(starting materials)
Intermediates
Conditions
+ concentrations and reaction times
Product
(target compound)
Output
Input

## Slide 19: Learning from experience
Published reaction data provides 200+ years of experience to learn from
Millions of tabulated reaction examples
reactants
major product
reagent(s)
catalyst(s)
solvent(s)
temperature
time
yield
provenance
concentrations
reaction mechanisms
byproducts
minor products
”failed” reactions
vessels
orders of addition

## Slide 20: Templates can (crudely) define the “rules” of chemistry
  Find core of transformation
1
  Add generalized neighbors
2
  Extend to known func. groups
3
[c:1]-[CH;@@;D3;+0:2]1-[O;H0;D2;+0]-[CH;@;D3;+0:3]-1-[c:4]
>>
[c:1]/[CH;D2;+0:2]=[CH;D2;+0:3]/[c:4]
  Canonicalize and record
4
Coley et al., J. Chem. Inf. Model. 2019, 59
Several prior publications
Segler and Waller, Chem. Eur. J. 2017, 23
Algorithmic extraction
“Template relevance” policy network training
Reaction templates are rigid subgraph pattern-matching rules that can be applied to novel molecules to generate hypothetical precursors

## Slide 21: Template-free models instead learn end-to-end
Tu and Coley, https://arxiv.org/abs/2110.09681
ClC1=NC=C(Br)C(NC2CCCC2)=N1
NC1CCCC1.ClC2=NC=C(Br)C(Cl)=N2
Product molecule
Reactant molecules
e.g., Graph2SMILES

## Slide 22: Applying retrosynthetic models recursively leads to full pathways to reasonably complex molecules
13 step synthetic pathway obtained in 60 seconds
Not the “best” pathway (e.g., shortest, cheapest, highest-yielding)
Only one of many possible pathways for a chemist to review
  Pathway ranking metrics mostly suitable for discovery chemistry, not process

## Slide 23: Multi-step planning tools do work for many compounds
The combinatorial explosion of options as we perform a retrosynthetic expansion is mitigated by tree search strategies (e.g., MCTS, best-first, proof number search)
Both data-driven and expert approaches have generated pathways that score well in blinded tests:
Segler, Preuss, Waller
Nature 555, 604-610 (2018)
Mikulak-Klucznik, Grzybowksi et al.
Nature 588, 83-88 (2020)
Because the search space grows exponentially with increasing depth (number of reactions), it’s essential to use a search policy; in practice, planning starts getting very expensive with ≥10 steps

## Slide 24: Synthesizable molecular design Using our knowledge of reactivity to define an accessible chemical space

## Slide 25: The downside of many de novo generation tools
These AI models optimize whatever black box function you tell them to; if that function doesn’t consider stability or synthesizability, then…*
SMILES GA suggestion scoring 0.881/1.000 on a standard benchmark task
Renz et al. 10.26434/chemrxiv.12213542.v1
Zhou et al., Sci. Rep. 2019, 9
Less obviously bad:

## Slide 26: Post hoc filtering of de novo generated molecules with our retrosynthetic planning engine
This doesn’t always work! For some design objectives, all of the top suggestions might be unsynthesizable
Gao and Coley, JCIM 2020

## Slide 27: Bottom-up generation with constraints on synthesizability
Constrained generative models enforce (mostly-)valid chemical reactions through expert templates or reaction prediction models
  Optimization of molecular structure  optimization of synthetic pathway
Bradshaw et al.’s MoleculeChef 2019
Korovina et al.’s ChemBO 2019
Gottipati et al.’s PGFS 2020
Horwood & Noutahi’s REACTOR 2020
Bradshaw et al.’s DAG-VAE 2020
See also

## Slide 28: Generation with explicit constraints on synthesizability
Optimization via conditional code
Reconstruction

## Slide 29: Connection to make-on-demand libraries
Reaction-based generative models are similar to “make-on-demand” libraries from combinatorial enumeration of building blocks subject to reaction rules
  Enamine’s REAL space includes ca. 20B molecules enumerated in this manner
  Generative models mitigate the need for enumeration by keeping this space implicit in the model
  This relies on the ability to predict products of reactions, which is an area of ongoing interest in molecular ML

## Slide 30: Prediction of organic reaction outcomes
To enumerate possible product molecules in a virtual enumeration setting
To evaluate the likelihood of a reaction’s success during synthesis planning
To identify impurities, side products, decomposition pathways, etc.
Output
Input
We have many input-output pairs, but don’t know how to write an exact function to relate them

## Slide 31: Formulating reaction prediction as graph edit prediction
One message passing network learns how atoms react
One message passing network learns to rank candidates
no descriptors;
just structure

## Slide 32: Formulating reaction prediction as graph edit prediction
One message passing network learns how atoms react
One message passing network learns to rank candidates
no descriptors;
just structure
Chart: MIT chemist participant
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | Model
Relaxed scoring | 0.575 | 0.51875 | 0.45625 | 0.65625 | 0.725 | 0.7 | 0.425 | 0.6375 | 0.2875 | 0.175 | 0.8 | 0.6875
(has seen 400k USPTO reactions)
Others have shown that these models can be pretrained on large datasets and fine-tuned on specific reaction families to overcome data sparsity issues

## Slide 33: Connecting design to automated execution Testing our designed molecules and synthetic routes in the lab

## Slide 34: Automatically validating molecular designs
Ideally, we would be able to validate the molecules designed by our generative models with minimal human intervention
  Closed-loop testing is the dream!
However, synthesis planning is far more than retrosynthesis
  What catalysts, solvents, reagents, temperature do we use?
  What concentrations and reaction time do we use?
  What kind of flask/vessel do we use, and how do we need to prepare it?
  What order do we add species in, and how quickly or slowly do we add them?
  How do we purify the desired product so we can use it in the next reaction?

## Slide 35: “Automated” laboratories have not automated planning
Processes are executed with minimal intervention, but are planned (semi)manually
Chemputer
Steiner et al., Science 2018, 363
AbbVie
Baranczak et al., ACS Med. Chem. Lett. 2017, 8
SRI’s AutoSyn
Collins et al., OPRD, 2020
ChemKonzert
Machida et al., Chem. Pharm. Bull. (Tokyo) 2010
MIT
Coley et al. Science 2019, 365
Lilly’s ASL
Godfrey et al., Drug. Discov. Today 2013, 18

## Slide 36: Even automated synthesis would not be enough to fully close the loop and “solve” lead optimization in drug discovery
Iterating through design-make-test cycles is still costly and time consuming
In an experimental drug discovery campaign, it’s typical to test O(1000) molecules, though some recent projects have reduced that to low 100s
Synthesis
Design
Validation
Modeling
Goal Definition
Functional Molecules

## Slide 37: Sample (in)efficiency of molecular optimization
Most papers on molecular optimization do not report the number of oracle calls
  When the oracle is a physical experiment or costly simulation, efficiency matters
Medicinal chemists are adept at pivoting from a “global” optimization to a “local” optimization around a promising core/scaffold with only dozens of experiments
Table 2 from Fu et al. “Differentiable Scaffolding Tree for Molecular Optimization”, arXiv:2109.10469 2021

## Slide 38: Conclusion Recontextualization

## Slide 39
Synthesis
Design
Validation
Understanding
Modeling
Goal Definition
Functional Molecules
Information
Modeling, molecular design, and molecular synthesis are key components of an autonomous discovery workflow
Collectively, data science tools can help us evaluate molecules designed in silico, propose/generate new ones, and plan how to synthesize and test them

## Slide 40: ccoley@mit.edu | coley.mit.edu | @cwcoley
Data:
CAS (current)
Pistachio (current)
Reaxys (former)
Machine Learning for Pharmaceutical Discovery and Synthesis
Klavs Jensen
William Green
Regina Barzilay
Tommi Jaakkola
Chris Voigt
Daniela Rus
Sangeeta Bhatia
Timothy Jamison
Vignesh Ram
Ava Soleimany
Alexander Amini
Natalie Eyke
Lucky Pattanaik
Wengong Jin
Hanyu Gao
Thomas Struble
Mike Fortunato
Yanfei Guan
Pieter Plehiers
John Schreck
Xiaoxue Wang
Yiming Mo
Dale Thomas
Justin Lummiss
Luke Rogers
Jon Jaworski
Chris Breen
Victor Schultz
Funding:
DARPA, MLPDS, ONR, NIH, NSF, Takeda, Nanite Bio, J-Clinic, MIT-IBM Watson AI Lab
Conflicts:
Entos, Galixir, Dow, Revela, Kebotix, Anagenex
Priyanka Raghavan
Wenhao Gao
Keir Adams
Tianyi Jin
Itai Levin
Zhengkai Tu
Aparajita Dasgupta
Sam Goldman
Rebecca Neeser
Thijs Stuyver
Matteo Aldeghi
Rocío Mercado
John Bradshaw
David Graff
Mingrou Xie
Jenna Fromer

## Slide 41: Additional questions
How do you foresee biological data standardization 10 years in the future? Will methods and practices be in place to support an emphasis on data-driven computations?
Do you think reactions generated by CASP with minimal human interaction should be eligible for intellectual property protections by the USPTO?
Could you explain how you deal with the lack of Deep Learning interpretability in drug design and development?

## Slide 42: Open Reaction Database https://open-reaction-database.org/
Data-driven methods for synthetic chemistry rely on … data
The ORD is an initiative to "support machine learning and related efforts in reaction prediction, chemical synthesis planning, and experiment design” by creating a schema for organic reaction data & establishing an open access repository
Governing Committee
Connor Coley (MIT)
Abby Doyle (UCLA, C-CAS)
Spencer Dreher (Merck)
Joel Hawkins (Pfizer)
Klavs Jensen (MIT)
Steven Kearnes (Relay)
Advisory Board
Juan Alvarez (Merck)
Alán Aspuru-Guzik (Toronto, MADNESS)
Tim Cernak (Michigan, Entos)
Lucy Colwell (Cambridge, SynTech, Google)
Werngard Czechtizky (AstraZeneca)
JW Feng (Google)
Matthew Gaunt (Cambridge, SynTech)
Alex Godfrey (NCATS)
Mimi Hii (Imperial, ROAR)
Greg Landrum (T5 Informatics)
Fabio Lima (Novartis)
Christos Nicolaou (Lilly)
Sarah Reisman (Caltech)
Matthew Sigman (Utah, C-CAS)
Jay Stevens (BMS)
Sarah Trice (Entos)
Matt Tudge (GSK)